## Slide 1: Introduction to VVUQ | Part 3 Validation
Task Group on VVUQ Concepts in Engineering Education
ASME Codes & Standards | Committee on Verification, Validation, and Uncertainty Quantification
Contacts: Lydia Stanford (stanfordl@asme.org) | Daniel Papert (papertd@asme.org​)
V. 3, Draft, 2026
© 2026 by ASME Task Group on VVUQ in Engineering Education is licensed under CC BY 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by/4.0/

## Slide 2: Outline
What is validation and why do we care?
How is validation performed?
What is prediction?
How does validation inform the model’s predictive capability?
v. 3, Draft, 2026

## Slide 3: What is model validation and why do we care?
Computational modeling and simulation are used to aid the decision-making process
  e.g., Predicting deformation of a structure: an inaccurate model could lead to poor decisions, potentially resulting in excessive deformation or even failure of a bridge or building.
Validation compares the simulation model results to real-world observations (data) to ensure it captures essential features (physical phenomena) of the real system.
Validation data should reflect the conditions of the intended use of the model.
  e.g., Assessing the predicted deformation of a structure against measured deformation under realistic or maximum loading conditions.
Model Input Data
Mathematical Model
Solution Verification
Experimental Data
Model Validation
Code Verification
Computational Model
Model Output Data
Aspects of validation:
Validation metrics
Metric threshold (decision-making)
Validation experiments (design of experiments)
Model output and experimental uncertainty
Intended use and extrapolation
v. 3, Draft, 2026

## Slide 4: How is validation performed?
Create model: build a computational model for a specific context of use
Verification: assess numerical errors (see previous module)
Collect measurements: conduct validation experiments (preferred) or collect historical data
Quantify uncertainty: estimate for both model outputs and measurements
Validation assessment/model error estimation: compare model outputs to measurements via
  qualitative assessment by expert judgment
  quantitative assessment using mathematical validation metrics
Note: There is often a hierarchy of validation in real-world complex systems
  validation of individual components or subsystems
  validation of the entire system
Create Model
Collect Measurements
Quantify Uncertainty
Model Error Estimation
Verification
v. 3, Draft, 2026

## Slide 5: How are validation experiments different from other experiments?
Traditional experiments/tests are conducted to:
  Improve physical understanding of the physical processes occurring
  Calibrate/update model input parameters
  Assess or certify system/subsystem performance or safety
Model validation experiments are conducted for the primary purpose of assessing the ability of the simulation model to predict the system responses for the experiment that is conducted.
Validation experiments can be conducted on the actual system of interest, but more commonly it is:
  A subsystem, assembly, or component of the actual system of interest
  The experimental conditions are not fully representative of the actual operating conditions of the system
Other important features of validation experiments:
  Experimental measurement uncertainty should be estimated in both the system response quantities of interest and the input quantities that are used the simulation model
  Quantitative methods should be used to assess the agreement between simulation and experimental results
  Blind model predictions of the validation experiment are the most informative of predictive capability
v. 3, Draft, 2026

## Slide 6: What is model prediction?
Prediction involves producing model outputs for which corresponding measured data is not available.
Validation domain: A model is validated against experimental results at a specific set of input conditions (‘validation points’) that form the validation domain.
Intended use domain: Predictions in the intended use domain of the model input space may be interpolative or extrapolative with respect to the validation domain.
Validation domain
Validation point
Intended use domain
Model Input 1
Model Input 2
Image credit: adapted from V&V 10
Model Input Settings for Prediction
v. 3, Draft, 2026

## Slide 7: What is predictive capability of a model?
Predictive capability is producing a simulation result, including all sources of uncertainty, at conditions where no experimental measurements are available.
Predictive capability is informed by:
  Quantitative validation assessment at conditions relevant to the prediction conditions of interest
  The similarity of the conditions at the prediction conditions to the model validation conditions
  The estimated magnitude of all the numerical solution uncertainties at the prediction conditions of interest
  The effect of the model input uncertainties at the prediction conditions of interest
  The uncertainty due to the model formulation itself, i.e., model form uncertainty
A simulation model’s adequacy for intended use involves diverse requirements such as:
  Requirements for model accuracy plus uncertainty at the prediction conditions of interest
  Economic, safety, and liability risks if the simulation model is potentially inaccurate
  Personnel, computer, and software costs to produce the simulation results
  Experience level required of the personnel to produce credible simulation results
v. 3, Draft, 2026

## Slide 8: References
ASME (2022), "Verification, Validation, and Uncertainty Quantification Terminology in Computational Modeling and Simulation," American Society of Mechanical Engineers, ASME VVUQ 1-2022, New York, NY.​
ASME (2019), "Standard for Verification and Validation in Computational Solid Mechanics." American Society of Mechanical Engineers, ASME Standard V&V 10-2019, New York, NY.​
ASME (2009), "Standard for Verification and Validation in Computational Fluid Dynamics and Heat Transfer." American Society of Mechanical Engineers, ASME Standard V&V 20-2009(R2021), New York, NY.​
Oberkampf, W. L. and C. J. Roy (2010), Verification and Validation in Scientific Computing, Cambridge University Press, UK.​
NaRC (2012), "Assessing the Reliability of Complex Models: Mathematical and Statistical Foundations of Verification, Validation, and Uncertainty Quantification." National Research Council of the National Academies, ISBN-13: 978-0-309-25634-6, Washington, DC.
v. 3, Draft, 2026