## Slide 1: Introduction to VVUQ | Part 4 Uncertainty Quantification
Task Group on VVUQ Concepts in Engineering Education
ASME Codes & Standards | Committee on Verification, Validation, and Uncertainty Quantification
Contacts: Lydia Stanford (stanfordl@asme.org) | Daniel Papert (papertd@asme.org​)
V. 3, Draft, 2026
© 2026 by ASME Task Group on VVUQ in Engineering Education is licensed under CC BY 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by/4.0/

## Slide 2: Outline
What is uncertainty quantification and why do we care?
Steps of uncertainty quantification and how it is performed
  Characterization of uncertainties
  Propagation of uncertainties
  Interpretation of uncertainties
Sensitivity Analysis
v. 3, Draft, 2026

## Slide 3: What is uncertainty quantification and why do we care?
Uncertainty Quantification (UQ) is the process of using statistical models to provide an estimate of uncertainty in the experimental and simulation results.
Uncertainty Quantification has three basic steps:
  Characterize Uncertainties: Identify all relevant uncertainties and characterize the uncertainties as much as is possible
  Propagate Uncertainties: Perform model evaluations to estimate the impact of model input uncertainties on the system response quantities of interest (QoIs)
  Interpret Results: Compute and explain the sources and impact of the uncertainties to the simulation customer
Uncertainty quantification is important because it informs the customer of the simulation results how the uncertainties impact the simulation results.
v. 3, Draft, 2026

## Slide 4: Characterize uncertainties
Model Input Data
Mathematical Model
Solution Verification
Experimental Data
Code Verification
Inputs
Parameters
Numerical
Measurement uncertainty
Uncertainty Quantification
Examples of model uncertainty:
Model form (physical assumptions/simplifications)
Parameters (calibration/tuning)
Numerical errors (solution errors, surrogate model errors, statistical sampling errors)
Examples of model input uncertainty:
Boundary/Initial conditions
Material properties
Geometry
Measurement uncertainty (inputs)
Examples of measurement uncertainty:
Limited number of measurements
Statistical sampling errors
Measurement bias
Data reduction
Model Validation
Computational Model
Model Output Data
Identify most import sources of uncertainties including inputs and parameters
Estimate the uncertainty in these values. Methods include calibration, data, subject matter expertise, first-principles, etc.
v. 3, Draft, 2026

## Slide 5: Propagate uncertainties and interpret results
Samples from uncertainties
Model Input Data
Mathematical Model
Inputs
Parameters
Numerical
Computational Model
Model Output Data
Model Input Data
Model Input Data
Model Input Data
Model Input Data
Uncertainty Quantification
Model Output Data
Model Output Data
Model Output Data
Model Output Data
Results can be interpreted in many ways including:
Mean and standard deviation
Median and other percentiles
Histogram or probability distribution
Take samples of uncertainty sources to create an ensemble of model inputs
Run each set of inputs through the model
Create an ensemble of model outputs
v. 3, Draft, 2026

## Slide 6: Rank the impact of uncertain inputs using sensitivity analysis
Closely related to UQ is Sensitivity Analysis where the importance of the model parameters are identified and potentially ranked.
Various approaches:
Local Sensitivity Analysis: Estimate sensitivity with small perturbations to the nominal model parameters
Global Sensitivity Analysis: Evaluate the sensitivity over the full range of the parameters
Sensitivity Analysis can be used to:
Select optimal design parameters to achieve system performance requirements
Identify the largest contributors to uncertainty in system responses
v. 3, Draft, 2026

## Slide 7: References
McClarren, R. G. (2018), Uncertainty Quantification and Predictive Computational Science, Springer, Cham, Switzerland.
Smith, R. C. (2014), Uncertainty Quantification: Theory, Implementation, and Applications, Society for Industrial and Applied Mathematics, Philadelphia, PA.
Saltelli, A., Ratto, M., Adres, T., Campolongo, F., Cariboni, J., Gatelli, D., Saisana, M., Taratola, S., (2008), Global Sensitivity Analysis. The Primer, Wiley, England.
ASME (2019), "Standard for Verification and Validation in Computational Solid Mechanics." American Society of Mechanical Engineers, ASME Standard V&V 10-2019, New York, NY.​
ASME (2021), "The Role of Uncertainty Quantification in Verification and Validation of Computational Solid Mechanics Models," American Society of Mechanical Engineers, ASME VVUQ 10.2-2021, New York, NY.
Oberkampf, W. L. and C. J. Roy (2010), Verification and Validation in Scientific Computing, Cambridge University Press, UK.​
NaRC (2012), "Assessing the Reliability of Complex Models: Mathematical and Statistical Foundations of Verification, Validation, and Uncertainty Quantification." National Research Council of the National Academies, ISBN-13: 978-0-309-25634-6, Washington, DC.
NA (2024), "Foundational Research Gaps and Future Directions for Digital Twins." National Academies of Sciences, Engineering and Medicine, DOI 10.17226/26894, Washington, DC.
v. 3, Draft, 2026